## Slide 1
CHAPTER 7
Logic, Shift, and Rotate Instructions

## Slide 2: Logic, Shift and Rotate
Boolean Data 0 or 1
  Requires only a single bit
  0 = FALSE
  1 = TRUE
Boolean operators
  Unary: NOT
  Binary: AND, OR, XOR

## Slide 3: Logic Instructions
and destination, source
  Logical AND
  can be used to clear specific destination bits
not destination
  Logical NOT (one's complement)
or destination, source
  Logical OR
  can be used to set specific destination bits
test destination, source
  Test bits
xor destination, source
  Logical Exclusive OR
  can be used to complement specific destination bits
selectively modify the bits
in the destination using
a bit pattern (mask)

## Slide 4: Destination and Source
AND destination, source
  destination = destination AND source
Destination :
  The result is stored in destination
  Must be register/ memory location
Source
  Can be a constant, register or memory location.
No memory to memory operation
Same with OR, XOR

## Slide 5: Examples
To clear the sign bit of al while leaving the other bits unchanged,
  01111111b = 7Fh (mask)
  and al,7Fh
To set the MSB and LSB of al while preserving the other bits,
  10000001b = 81h (mask)
  or al,81h
To change the sign bit of dx,
  8000h (mask).
  xor dx,8000h

## Slide 6: The TEST instruction
TEST destination, source
  Performs AND, does not store result
  Flags are set as if the AND were executed
Example
TEST CL, 10000001b JZ EvenAndNonNegative JS Negative ; must be odd and positive if it gets here

## Slide 7: The NOT Instruction
1’s complement
Flips every bit
NO EFFECT ON STATUS FLAGS

## Slide 8: Bit Shifting
Slide bits in byte or word to left or right
  What happens to bit that is shifted out?
    It is copied into the CF
  What bit value is shifted in?
    SHR, SHL, SAL: =0
    SAR: =sign bit
    ROR, ROL: =bit shifted out
    RCR, RCL: =CF

## Slide 9: Left Shift Instructions
SHL
  Zeros are shifted into the rightmost bit positions
  last bit shifted out goes into CF
Effect on flags:
  SF, PF, ZF reflect the result
  AF is undefined
  CF = last bit shifted out
  OF = 1 if result changes sign on last shift
dh = 10001010, cl = 00000011
after shl dh,cl
  dh = 01010000, cf = 0

## Slide 10: The SAL instruction
shl :multiply an operand by powers of 2
sal(shift arithmetic left)
  used in instances where multiplication is intended
Both instructions generate the same machine code!

## Slide 11: Right Shifts
SHR – for logical shifting and unsigned division
SAR – for signed division

## Slide 12: Rotate
Rotate Instructions Rotate Left
  rol (rotate left) shifts bits to the left
  The msb is shifted into the rightmost bit
  The cf also gets the the bit shifted out of the msb
Rotate Right
  ror (rotate right) rotates bits to the right
  the rightmost bit is shifted into the msb
  into cf

## Slide 13: Rotate through Carry
Rotate through Carry Left
  The instruction rcl shifts bits to the left
  The msb is shifted into cf
  cf is shifted into the rightmost bit
Rotate through Carry Right
  rcr rotates bits to the right
  The lsb bit is shifted into cf
  cf is shifted into the msb
Refer to figure 7.5 to 7.8 for the illustrations

## Slide 14: CHAPTER 9 Multiplication and Division Instructions

## Slide 15: Signed Vs Unsigned Multiplication
Signed and Unsigned numbers must be interpreted accordingly
P = 10000000 * 11111111
Unsigned Interpretation
  P = 128 * 255 = 32640
Signed Interpretation
  P = -128 * -1 = 128
Hence
  P = 0111111110000000b ; unsigned multiplication
  P = 0000000010000000b ; signed multiplication
PRODUCT IS DIFFERENT with respect to INTERPRETATION ( for numbers that are negative )

## Slide 16: Multiplication instructions
imul source
  Signed multiply [Integer MULtiply]
mul source
  Unsigned multiply
Byte and Word Multiplication (A X B)
  If two bytes are multiplied, the result is a 16-bit word
    A: source
    B: AL
    product: AX
  If two words are multiplied, the result is a 32-bit doubleword
    A: source
    B: AX
    Product: DX:AX
      Product (ms 16 bits): DX
      Product (ls 16 bits): AX

## Slide 17: Multiplication instructions
source can be a register or memory byte/word, but can not be a constant
Byte form
  AX=AL*source
Word form
  DX:AX=AX*source
CF/OF
  MUL
    0: upper half result 0
  IMUL
    0: if upper half is sign extension of lower half.
  CF/OF = 1 means product is too big for lower half of the destination (AL for byte and AX for word)
If ax contains 0001h and bx contains FFFFh
  mul bx; dx = 0000h ax = FFFFh
  imul bx ; dx = FFFFh ax = FFFFh (-1)
SF, ZF, AF, and PF
  Undefined

## Slide 18: More Examples
Instruction | Hex Product | DX | AX | CF/OF
MUL BX | FFFE0001 (4294836225) | FFFE (!zero) | 0001 | 1
IMUL BX | 1 | 0000 | 0001 | 0
AX=FFFFh,BX=FFFFh
AX=80h,BX=FFh
Instruction | Hex Product | AH | AL | CF/OF
MUL BX | 7F80 (128) | 7F(!zero) | 80 | 1
IMUL BX | 0080 | 00 (no sign extension) | 80 | 1

## Slide 19: Division instructions
cbw
  convert byte to word
cwd
  convert word to doubleword
div source
  unsigned divide
idiv source
  signed divide

## Slide 20: Byte and Word Division (A/B)
When division is performed
  two results: the quotient and the remainder
  Quotient and remainder are same size as the divisor
  Divisor can not be a constant

## Slide 21: Byte and Word Division (A/B) (contd.)
For the byte form,
  Divisor, B: source ;Dividend , A: AX
  Quotient : AL ;Remainder: AH
  AL = AX / divisor; divisor is BYTE
  AH = AX % divisor;
For the word form,
  Divisor, B: source ;Dividend , A: DX:AX
  Quotient: AX ; Remainder: DX
  AX = DX:AX / divisor ; divisor is WORD
  DX = DX:AX % divisor

## Slide 22: An Example
;If dx = 0000h, ax = 0005h, and
bx = FFFEh (-2)
div bx; ax = 0000h dx = 0005h
idiv bx; ax = FFFEh dx = 0001h

## Slide 23: Divide Overflow
It is possible that the quotient will be too big to fit in the specified destination (al or ax)
if the divisor is much smaller than the dividend
the program terminates and the system displays the message "Divide Overflow"

## Slide 24: Sign Extension of the Dividend
Word division
  The dividend is in dx:ax even if the actual dividend will fit in ax
  For div, dx should be cleared
  For idiv, dx should be made the sign extension of ax using cwd
e.g. -1250/7
MOV AX,-1250
CWD ; sign extend
MOV BX,7
IDIV BX

## Slide 25: Sign Extension of the Dividend
Byte division
  The dividend is in ax even if the actual dividend will fit in al
  For div, ah should be cleared
  For idiv, ah should be made the sign extension of al using cbw

## Slide 26: Thank You